## Slide 1: COMP 590-154: Computer Architecture
Speculation and Traps in Out-of-Order Cores

## Slide 2: What is wrong with Tomasulo’s?
Branch instructions
  Need branch prediction to guess what to fetch next
  Need speculative execution to “clean up” wrong guesses
Exceptions and Traps (“software” interrupts)
  Need to handle uncommon execution cases
    Jump to a software handler
  Should follow the insn. on which they were triggered
  Often referred to as precise interrupts
  Don’t know relative order of instructions in RS

## Slide 3: Speculation and Precise Interrupts
When branch is mis-speculated by predictor
  Must reset state (e.g,. regs) to time of branch
Sequential semantics for interrupts
  All insns. before interrupt should be complete
  All insns. after interrupt should look as if never started (abort)
What makes this difficult?
  Younger insns. finish before branch  must undo writebacks
  Older insns. not done when young branch resolves  must wait
    Older insn. takes page fault or divide by zero  forget the branch
  Same problem  Same solution

## Slide 4: Precise State
Speculative execution requires
  (Ability to) abort & restart at every branch
  Abort & restart at every load (covered in later lecture)
Synchronous (exception and trap) events require
  Abort & restart at every load, store, divide, …
Asynchronous (hardware) interrupts require
  Abort & restart at every ??
Real world: bite the bullet
  Implement abort & restart at every insn.
  Called precise state

## Slide 5: Precise State Implementation Options
Imprecise state: ignore the problem!
  Makes page faults (any restartable exceptions) difficult
  Makes speculative execution practically impossible
Force in-order completion (W): stall pipe if necessary
  Slow (takes away benefit of Out-of-Order)
Keep track of precise state in hardware
  Reset current state from precise state when needed
  Everything is better in hardware

## Slide 6: Our-of-Order Topics
“Scoreboarding”
  First OoO, no register renaming
“Tomasulo’s algorithm”
  OoO with register renaming
Handling precise state and speculation
  P6-style execution (Intel Pentium Pro)
  R10k-style execution (MIPS R10k)
Handling memory dependencies

## Slide 7: The Problem with Precise State
Problem: writeback combines two functions
  Forward values to younger insns.: out-of-order is OK
  Write values to registers: needs to be in order
Similar solution as for OoO decode
  Split writeback into two stages
regfile
L1-D
I$
B
P
insn buffer

## Slide 8: Re-Order Buffer (ROB)
Insn. buffer  Re-Order Buffer (ROB)
  Buffer completed results en route to register file
  Can be merged with RS (RUU) or separate (common today)
Split writeback (W) into two stages
  Why is there no latch between W1 and W2?
regfile
L1-D
I$
B
P
Re-Order Buffer (ROB)

## Slide 9: Complete and Retire
Complete (C): insns. write results into ROB
  Out-of-order: don’t block younger insns.
Retire (R): a.k.a. commit
  ROB writes results to register file
  In order: stall back-propagates to younger insns.
regfile
L1-D
I$
B
P
Re-Order Buffer (ROB)
C
R

## Slide 10: P6 Data Structures
P6: Start with Tomasulo’s algorithm… add ROB
ROB (separate from RS)
  head, tail: pointers maintain sequential order
  R: insn. output register, V: insn. output value
Tags are different
  Tomasulo: RS#  P6: ROB#
Map Table is different
  T+: tag + “ready-in-ROB” bit
    T==0  Value is ready in register file
    T!=0  Value is not ready
    T!=0+  Value is ready in the ROB

## Slide 11: P6 Data Structures (1/2)
value
V1
V2
FU
T+
T2
T1
T
op
==
==
==
==
Map Table
RS
CDB.V
CDB.T
Dispatch
Regfile
T
==
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch

## Slide 12: P6 Data Structures (2/2)
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 |  |  |  |  | 
 | 2 | mulf f0,f1,f2 |  |  |  |  | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | 
f2 | 
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | no |  |  |  |  |  | 
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V

## Slide 13: P6 Pipeline
New pipeline structure: F, D, S, X, C, R
  D (dispatch)
    Structural hazard (ROB/RS) ? stall
    Allocate ROB/RS
    Set RS tag to ROB#
    Set Map Table entry to ROB# and clear “ready-in-ROB” bit
    Read ready registers into RS (from either ROB or Regfile)
  X (execute)
    Free RS entry
      No need to wait for W, because tag is from ROB instead of RS

## Slide 14: P6 Pipeline
C (complete)
  Structural hazard (CDB)? wait
  Write value into ROB entry for RS tag
  If Map Table has same entry, set “ready-in-ROB” bit (+)
R (retire)
  Insn. at ROB head not complete ? stall
  Handle any exceptions
    Some go before instruction (branch mispredict, page fault) – why?
    Some go after instruction (e.g., trap) – why?
  ROB head value  Regfile
  Free ROB entry

## Slide 15: P6 Dispatch (D) (1/2)
RS/ROB full ? stall
Allocate RS/ROB entries, assign ROB# to RS output tag
Map Table entry set to ROB#, clear “ready-in-ROB”
value
V1
V2
FU
T+
T2
T1
T
op
==
==
==
==
Map Table
RS
CDB.V
CDB.T
Dispatch
Regfile
T
==
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch

## Slide 16: P6 Dispatch (D) (2/2)
Read tags for register inputs from Map Table
  Tag==0  value from Regfile (not shown)
  Tag!=0  Map Table tag to RS, Tag!=0+  value from ROB
value
V1
V2
FU
T+
T2
T1
T
op
==
==
==
==
Map Table
RS
CDB.V
CDB.T
Dispatch
Regfile
T
==
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch

## Slide 17: P6 Complete (C)
CDB busy ? stall : broadcast <value,tag> on CDB
Result  ROB, if Map Table valid  “ready-in-ROB” bit
If RS T1 or T2 matches, write CDB.V into RS slot
value
V1
V2
FU
T+
T2
T1
T
op
==
==
==
==
Map Table
RS
CDB.V
CDB.T
Dispatch
Regfile
T
==
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch

## Slide 18: P6 Retire (R)
ROB head not complete ? stall : free ROB entry
Write ROB head result to Regfile
If still valid, clear Map Table entry
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
RS
CDB.V
CDB.T
Dispatch
Regfile
T
==
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch

## Slide 19: P6: Cycle 1
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
ht | 1 | ldf X(r1),f1 | f1 |  |  |  | 
 | 2 | mulf f0,f1,f2 |  |  |  |  | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#1
f2 | 
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | ROB#1 |  |  |  | [r1]
3 | ST | no |  |  |  |  |  | 
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate
set ROB# tag

## Slide 20: P6: Cycle 2
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
h | 1 | ldf X(r1),f1 | f1 |  | c2 |  | 
t | 2 | mulf f0,f1,f2 | f2 |  |  |  | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#1
f2 | ROB#2
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | ROB#1 |  |  |  | [r1]
3 | ST | no |  |  |  |  |  | 
4 | FP1 | yes | mulf | ROB#2 |  | ROB#1 | [f0] | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate
set ROB# tag

## Slide 21: P6: Cycle 3
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
h | 1 | ldf X(r1),f1 | f1 |  | c2 | c3 | 
 | 2 | mulf f0,f1,f2 | f2 |  |  |  | 
t | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#1
f2 | ROB#2
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#3 | ROB#2 |  |  | [r1]
4 | FP1 | yes | mulf | ROB#2 |  | ROB#1 | [f0] | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate
free

## Slide 22: P6: Cycle 4
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | yes | add | ROB#4 |  |  | [r1] | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#3 | ROB#2 |  |  | [r1]
4 | FP1 | yes | mulf | ROB#2 |  | ROB#1 | [f0] | CDB.V
5 | FP2 | no |  |  |  |  |  | 
allocate
ROB#1 ready
grab CDB.V
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
h | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | f2 |  | c4 |  | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
t | 4 | addi r1,4,r1 | r1 |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#1+
f2 | ROB#2
r1 | ROB#4
CDB | 
T | V
ROB#1 | [f1]
ldf finished
set “ready-in-ROB” bit
write result to ROB
CDB broadcast

## Slide 23: P6: Cycle 5
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
h | 2 | mulf f0,f1,f2 | f2 |  | c4 | c5 | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 | r1 |  | c5 |  | 
t | 5 | ldf X(r1),f1 | f1 |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#5
f2 | ROB#2
r1 | ROB#4
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | yes | add | ROB#4 |  |  | [r1] | 
2 | LD | yes | ldf | ROB#5 |  | ROB#4 |  | 
3 | ST | yes | stf | ROB#3 | ROB#2 |  |  | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate
free
ldf retires
write ROB result to regfile

## Slide 24: P6: Cycle 6
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
h | 2 | mulf f0,f1,f2 | f2 |  | c4 | c5+ | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 | r1 |  | c5 | c6 | 
 | 5 | ldf X(r1),f1 | f1 |  |  |  | 
t | 6 | mulf f0,f1,f2 | f2 |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#5
f2 | ROB#6
r1 | ROB#4
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | ROB#5 |  | ROB#4 |  | 
3 | ST | yes | stf | ROB#3 | ROB#2 |  |  | [r1]
4 | FP1 | yes | mulf | ROB#6 |  | ROB#5 | [f0] | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate
free

## Slide 25: P6: Cycle 7
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | ROB#5 |  | ROB#4 |  | CDB.V
3 | ST | yes | stf | ROB#3 | ROB#2 |  |  | [r1]
4 | FP1 | yes | mulf | ROB#6 |  | ROB#5 | [f0] | 
5 | FP2 | no |  |  |  |  |  | 
ROB#4 ready
grab CDB.V
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
h | 2 | mulf f0,f1,f2 | f2 |  | c4 | c5+ | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 | r1 | [r1] | c5 | c6 | c7
 | 5 | ldf X(r1),f1 | f1 |  | c7 |  | 
t | 6 | mulf f0,f1,f2 | f2 |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#5
f2 | ROB#6
r1 | ROB#4+
CDB | 
T | V
ROB#4 | [r1]
stall D (no free STore RS)

## Slide 26: P6: Cycle 8
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#3 | ROB#2 |  | [f2] | [r1]
4 | FP1 | yes | mulf | ROB#6 |  | ROB#5 | [f0] | 
5 | FP2 | no |  |  |  |  |  | 
ROB#2 ready
grab CDB.V
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
h | 2 | mulf f0,f1,f2 | f2 | [f2] | c4 | c5+ | c8
 | 3 | stf f2,Z(r1) |  |  | c8 |  | 
 | 4 | addi r1,4,r1 | r1 | [r1] | c5 | c6 | c7
 | 5 | ldf X(r1),f1 | f1 |  | c7 | c8 | 
t | 6 | mulf f0,f1,f2 | f2 |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#5
f2 | ROB#6
r1 | ROB#4+
CDB | 
T | V
ROB#2 | [f2]
stall R for addi (in-order)
ROB#2 not in MapTable f2,
don’t set “ready-in-ROB”

## Slide 27: P6: Cycle 9
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#7 | ROB#6 |  |  | ROB#4.V
4 | FP1 | yes | mulf | ROB#6 |  | ROB#5 | [f0] | CDB.V
5 | FP2 | no |  |  |  |  |  | 
ROB#5 ready
grab CDB.V
free, re-allocate
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | f2 | [f2] | c4 | c5+ | c8
h | 3 | stf f2,Z(r1) |  |  | c8 | c9 | 
 | 4 | addi r1,4,r1 | r1 | [r1] | c5 | c6 | c7
 | 5 | ldf X(r1),f1 | f1 | [f1] | c7 | c8 | c9
 | 6 | mulf f0,f1,f2 | f2 |  | c9 |  | 
t | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#5+
f2 | ROB#6
r1 | ROB#4+
CDB | 
T | V
ROB#5 | [f1]
retire mulf
all pipe stages active at once!

## Slide 28: P6: Cycle 10
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | f2 | [f2] | c4 | c5+ | c8
h | 3 | stf f2,Z(r1) |  |  | c8 | c9 | c10
 | 4 | addi r1,4,r1 | r1 | [r1] | c5 | c6 | c7
 | 5 | ldf X(r1),f1 | f1 | [f1] | c7 | c8 | c9
 | 6 | mulf f0,f1,f2 | f2 |  | c9 | c10 | 
t | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#5+
f2 | ROB#6
r1 | ROB#4+
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#7 | ROB#6 |  |  | ROB#4.V
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
free

## Slide 29: P6: Cycle 11
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | f2 | [f2] | c4 | c5 | c8
 | 3 | stf f2,Z(r1) |  |  | c8 | c9 | c10
h | 4 | addi r1,4,r1 | r1 | [r1] | c5 | c6 | c7
 | 5 | ldf X(r1),f1 | f1 | [f1] | c7 | c8 | c9
 | 6 | mulf f0,f1,f2 | f2 |  | c9 | c10 | 
t | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#5+
f2 | ROB#6
r1 | ROB#4+
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#7 | ROB#6 |  |  | ROB#4.V
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
retire stf

## Slide 30: Precise State in P6
Point of ROB is maintaining precise state
  How does that work?
    Wait until last good insn. retires, first bad insn. at ROB head
    Zero (0) contents of ROB, RS, and Map Table
    Start over
  Works because zero (0) means the right thing…
    0 in ROB/RS  entry is empty
    Tag == 0 in Map Table  register is in Regfile
  …and because Regfile and L1-D writes take place at R
  Example: page fault in first stf

## Slide 31: P6: Cycle 9 (with precise state)
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | f2 | [f2] | c4 | c5+ | c8
h | 3 | stf f2,Z(r1) |  |  | c8 | c9 | 
 | 4 | addi r1,4,r1 | r1 | [r1] | c5 | c6 | c7
 | 5 | ldf X(r1),f1 | f1 | [f1] | c7 | c8 | c9
 | 6 | mulf f0,f1,f2 | f2 |  | c9 |  | 
t | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | ROB#5+
f2 | ROB#6
r1 | ROB#4+
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#7 | ROB#6 |  |  | ROB#4.V
4 | FP1 | yes | mulf | ROB#6 |  | ROB#5 | [f0] | CDB.V
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
ROB#5 | [f1]
PAGE FAULT

## Slide 32: P6: Cycle 10 (with precise state)
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | f2 | [f2] | c4 | c5+ | c8
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | 
f2 | 
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | no |  |  |  |  |  | 
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
faulting insn at ROB head?
CLEAR EVERYTHING
set fetch PC to fault handler

## Slide 33: P6: Cycle 11 (with precise state)
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | f2 | [f2] | c4 | c5+ | c8
ht | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | 
f2 | 
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#3 |  |  | [f4] | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
PF handler done?
CLEAR EVERYTHING
iret fetch PC to faulting insn.

## Slide 34: P6: Cycle 12 (with precise state)
ROB |  |  |  |  |  |  | 
ht | # | Insn | R | V | S | X | C
 | 1 | ldf X(r1),f1 | f1 | [f1] | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | f2 | [f2] | c4 | c5+ | c8
h | 3 | stf f2,Z(r1) |  |  | c12 |  | 
t | 4 | addi r1,4,r1 | r1 |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | 
f1 | 
f2 | 
r1 | ROB#4
Reservation Stations |  |  |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2 | V1 | V2
1 | ALU | yes | addi | ROB#4 |  |  | [r1] | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | ROB#3 |  |  | [f4] | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V

## Slide 35: P6 Performance
In other words: what is the cost of precise state?
  In general: same performance as “plain” Tomasulo
    ROB is not a performance device
    Maybe a little better (RS freed earlier  fewer struct hazards)
  Unless ROB is too small
    In which case ROB struct hazards become a problem
  Rules of thumb for ROB size
    At least N (width) * number of pipe stages between D and R
    At least N * thit-L2
    Can add a factor of 2 to both if you want
    What is the rationale behind these?

## Slide 36: The Problem with P6
Problem for high performance implementations
  Too much value movement (Regfile/ROBRSROBRegfile)
  Multi-input muxes, long buses, slow clock
value
V1
V2
FU
T+
T2
T1
T
op
==
==
==
==
Map Table
RS
CDB.V
CDB.T
Dispatch
Regfile
T
==
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch

## Slide 37: MIPS R10K: Alternative Implementation
One big physical register file holds all data - no copies
  Register file close to FUs  small and fast data path
  ROB and RS “on the side” used only for control and tags
FU
T+
T2+
T1+
T
op
==
==
==
==
Map Table
RS
CDB.T
Dispatch
T
==
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch
Told
T
T
Free
List
T
Arch.
Map
Regfile

## Slide 38: Register Renaming in R10K
Architectural register file? Gone
Physical register file holds all values
  #physical registers = #architectural registers + #ROB entries
  Map architectural registers to physical registers
  No WAW or WAR hazards (physical regs. replace RS values)
Fundamental change to map table
  Mappings cannot be 0 (no architectural register file)
Explicit free list tracks unallocated physical regs.
  ROB returns physical regs. to free list

## Slide 39: Register Renaming
Example
  Names: r1,r2,r3 Locations: p1,p2,p3,p4,p5,p6,p7
  Original: r1p1, r2p2, r3p3, p4–p7 are “free”
Question: how is the last add renamed?
  We are out of free physical registers
  Real question: how/when are physical registers freed?
MapTable |  |  |  | FreeList |  | Original insns. |  | Renamed insns.
r1 | r2 | r3 |  |  |  |  |  | 
p1 | p2 | p3 |  | p4,p5,p6,p7 |  | add r2,r3,r1 |  | add p2,p3,p4
p4 | p2 | p3 |  | p5,p6,p7 |  | sub r2,r1,r3 |  | sub p2,p4,p5
p4 | p2 | p5 |  | p6,p7 |  | mul r2,r3,r3 |  | mul p2,p5,p6
p4 | p2 | p6 |  | p7 |  | div r1,4,r1 |  | div p4,4,p7
p7 | p2 | p6 |  |  |  | add r1,r3,r2 |  | add p7,p6,???

## Slide 40: Register Renaming
Example
  Names: r1,r2,r3 Locations: p1,p2,p3,p4,p5,p6,p7
  Original: r1p1, r2p2, r3p3, p4–p7 are “free”
Question: how is the last add renamed?
  We are out of free physical registers
  Real question: how/when are physical registers freed?
MapTable |  |  |  | FreeList |  | Original insns. |  | Renamed insns.
r1 | r2 | r3 |  |  |  |  |  | 
p1 | p2 | p3 |  | p4,p5,p6,p7 |  | add r2,r3,r1 |  | add p2,p3,p4
p4 | p2 | p3 |  | p5,p6,p7 |  | sub r2,r1,r3 |  | sub p2,p4,p5
p4 | p2 | p5 |  | p6,p7 |  | mul r2,r3,r3 |  | mul p2,p5,p6
p4 | p2 | p6 |  | p7 |  | div r1,4,r1 |  | div p4,4,p7
p7 | p2 | p6 |  |  |  | add r1,r3,r2 |  | add p7,p6,???

## Slide 41: Physical Register Reclamation
P6
  No need to free speculative (“in-flight”) values explicitly
  Temporary storage comes with ROB entry
R10K
  Can’t free physical regs. when insn. retires
    Younger insns. likely depend on it
  But…
    Can free physical reg. previously mapped to same logical reg.
    Why?

## Slide 42: Freeing Registers in R10K
When add retires, free p1
When sub retires, free p3
When mul retires, free p5
When div retires, free p4
MapTable |  |  |  | FreeList |  | Original insns. |  | Renamed insns.
r1 | r2 | r3 |  |  |  |  |  | 
p1 | p2 | p3 |  | p4,p5,p6,p7 |  | add r2,r3,r1 |  | add p2,p3,p4
p4 | p2 | p3 |  | p5,p6,p7 |  | sub r2,r1,r3 |  | sub p2,p4,p5
p4 | p2 | p5 |  | p6,p7 |  | mul r2,r3,r3 |  | mul p2,p5,p6
p4 | p2 | p6 |  | p7 |  | div r1,4,r1 |  | div p4,4,p7
p7 | p2 | p6 |  | p1 |  | add r1,r3,r2 |  | add p7,p6,p1
  Always OK to free old mapping

## Slide 43: R10K Data Structures
New tags (again)
  P6: ROB#  R10K: PR#
ROB
  T: physical register corresponding to insn’s logical output
  Told: physical register previously mapped to insn’s logical output
RS
  T, T1, T2: output, input physical registers
Map Table
  T+: PR# (never empty) + “ready” bit
Architectural Map Table
  T: PR# (never empty)
Free List
  T: PR#
  No values in ROB, RS, or on CDB

## Slide 44: R10K Data Structures
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
 | 1 | ldf X(r1),f1 |  |  |  |  | 
 | 2 | mulf f0,f1,f2 |  |  |  |  | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#2+
f2 | PR#3+
r1 | PR#4+
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | no |  |  |  | 
2 | LD | no |  |  |  | 
3 | ST | no |  |  |  | 
4 | FP1 | no |  |  |  | 
5 | FP2 | no |  |  |  | 
CDB
T
Notice I: no values anywhere
Free List
PR#5,PR#6,PR#7,PR#8
Notice II: MapTable is never empty
Arch. Map | 
Reg | T+
f0 | PR#1
f1 | PR#2
f2 | PR#3
r1 | PR#4

## Slide 45: R10K Pipeline
R10K pipeline structure: F, D, S, X, C, R
  D (dispatch)
    Structural hazard (RS, ROB, physical registers) ? stall
    Allocate RS, ROB, and new physical register (T)
    Record previously mapped physical register (Told)
  C (complete)
    Write destination physical register
  R (retire)
    ROB head not complete ? stall
    Handle any exceptions
    Free ROB entry
    Free previous physical register (Told)
    Record committed physical register (T)

## Slide 46: R10K Dispatch (D)
Read preg (physical register) tags for input registers, store in RS
Read preg tag for output register, store in ROB (Told)
Allocate new preg (free list) for output reg, store in RS, ROB, Map Table
FU
T+
T2+
T1+
T
op
==
==
==
==
Map Table
RS
CDB.T
Dispatch
T
==
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch
Told
T
T
Free
List
T
Arch.
Map
Regfile

## Slide 47: R10K Complete (C)
Set insn’s output register ready bit in map table
Set ready bits for matching input tags in RS
FU
T+
T2+
T1+
T
op
==
==
==
==
Map Table
RS
CDB.T
Dispatch
T
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch
Told
T
T
Free
List
T
Arch.
Map
==
Regfile

## Slide 48: R10K Retire (R)
Return Told of ROB head to free list
Record T of ROB head in architectural map table
FU
T+
T2+
T1+
T
op
==
==
==
==
Map Table
RS
CDB.T
Dispatch
T
==
==
==
R
value
ROB
Head
Retire
Tail
Dispatch
Told
T
T
Free
List
T
Arch.
Map
==
Regfile

## Slide 49: R10K: Cycle 1
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
ht | 1 | ldf X(r1),f1 | PR#5 | PR#2 |  |  | 
 | 2 | mulf f0,f1,f2 |  |  |  |  | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#5
f2 | PR#3+
r1 | PR#4+
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | no |  |  |  | 
2 | LD | yes | ldf | PR#5 |  | PR#4+
3 | ST | no |  |  |  | 
4 | FP1 | no |  |  |  | 
5 | FP2 | no |  |  |  | 
Allocate new preg (PR#5) to f1
Free List
PR#5,PR#6,PR#7,PR#8
Remember old preg mapped to
f1 (PR#2) in ROB
CDB
T
Arch. Map | 
Reg | T+
f0 | PR#1
f1 | PR#2
f2 | PR#3
r1 | PR#4

## Slide 50: R10K: Cycle 2
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
h | 1 | ldf X(r1),f1 | PR#5 | PR#2 | c2 |  | 
t | 2 | mulf f0,f1,f2 | PR#6 | PR#3 |  |  | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#5
f2 | PR#6
r1 | PR#4+
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | no |  |  |  | 
2 | LD | yes | ldf | PR#5 |  | PR#4+
3 | ST | no |  |  |  | 
4 | FP1 | yes | mulf | PR#6 | PR#1+ | PR#5
5 | FP2 | no |  |  |  | 
Allocate new preg (PR#6) to f2
Free List
PR#6,PR#7,PR#8
Remember old preg mapped to
f3 (PR#3) in ROB
CDB
T
Arch. Map | 
Reg | T+
f0 | PR#1
f1 | PR#2
f2 | PR#3
r1 | PR#4

## Slide 51: R10K: Cycle 3
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
h | 1 | ldf X(r1),f1 | PR#5 | PR#2 | c2 | c3 | 
 | 2 | mulf f0,f1,f2 | PR#6 | PR#3 |  |  | 
t | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#5
f2 | PR#6
r1 | PR#4+
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | no |  |  |  | 
2 | LD | no |  |  |  | 
3 | ST | yes | stf |  | PR#6 | PR#4+
4 | FP1 | yes | mulf | PR#6 | PR#1+ | PR#5
5 | FP2 | no |  |  |  | 
Stores are not allocated pregs
Free List
PR#7,PR#8, PR#9
Free
CDB
T
Arch. Map | 
Reg | T+
f0 | PR#1
f1 | PR#2
f2 | PR#3
r1 | PR#4

## Slide 52: R10K: Cycle 4
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
h | 1 | ldf X(r1),f1 | PR#5 | PR#2 | c2 | c3 | c4
 | 2 | mulf f0,f1,f2 | PR#6 | PR#3 | c4 |  | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
t | 4 | addi r1,4,r1 | PR#7 | PR#4 |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#5+
f2 | PR#6
r1 | PR#7
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | yes | addi | PR#7 | PR#4+ | 
2 | LD | no |  |  |  | 
3 | ST | yes | stf |  | PR#6 | PR#4+
4 | FP1 | yes | mulf | PR#6 | PR#1+ | PR#5+
5 | FP2 | no |  |  |  | 
ldf completes
set MapTable ready bit
Free List
PR#7,PR#8, PR#9
Match PR#5 tag from CDB & issue
CDB
T
PR#5
Arch. Map | 
Reg | T+
f0 | PR#1
f1 | PR#2
f2 | PR#3
r1 | PR#4

## Slide 53: R10K: Cycle 5
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
 | 1 | ldf X(r1),f1 | PR#5 | PR#2 | c2 | c3 | c4
h | 2 | mulf f0,f1,f2 | PR#6 | PR#3 | c4 | c5 | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 | PR#7 | PR#4 | c5 |  | 
t | 5 | ldf X(r1),f1 | PR#8 | PR#5 |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#8
f2 | PR#6
r1 | PR#7
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | yes | addi | PR#7 | PR#4+ | 
2 | LD | yes | ldf | PR#8 |  | PR#7
3 | ST | yes | stf |  | PR#6 | PR#4+
4 | FP1 | no |  |  |  | 
5 | FP2 | no |  |  |  | 
ldf retires
Return PR#2 to free list
Record PR#5 in Arch map
Free List
PR#8,PR#2, PR#9
Free
CDB
T
Arch. Map | 
Reg | T+
f0 | PR#1
f1 | PR#5
f2 | PR#3
r1 | PR#4

## Slide 54: Precise State in R10K
Precise state is more difficult in R10K
  Physical registers are written out-of-order (at C)
  Roll back the Map Table, Arch Table, Free List
    “free” written registers and “restore” old ones
Two ways of restoring Map Table and Free List
  Option I: serial rollback using T, Told ROB fields
    Slow, but simple
  Option II: single-cycle restoration from some checkpoint
    Fast, but checkpoints are expensive
  Modern processor compromise: make common case fast
    Checkpoint only (low-confidence) branches (frequent rollbacks)
    Serial recovery for page-faults and interrupts (rare rollbacks)

## Slide 55: R10K: Cycle 5 (with precise state)
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
 | 1 | ldf X(r1),f1 | PR#5 | PR#2 | c2 | c3 | c4
h | 2 | mulf f0,f1,f2 | PR#6 | PR#3 | c4 | c5 | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 | PR#7 | PR#4 | c5 |  | 
t | 5 | ldf X(r1),f1 | PR#8 | PR#5 |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#8
f2 | PR#6
r1 | PR#7
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | yes | addi | PR#7 | PR#4+ | 
2 | LD | yes | ldf | PR#8 |  | PR#7
3 | ST | yes | stf |  | PR#6 | PR#4+
4 | FP1 | no |  |  |  | 
5 | FP2 | no |  |  |  | 
CDB
T
undo insns 3-5
(doesn’t matter why)
use serial rollback
Free List
PR#8,PR#2, PR#9

## Slide 56: R10K: Cycle 6 (with precise state)
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
 | 1 | ldf X(r1),f1 | PR#5 | PR#2 | c2 | c3 | c4
h | 2 | mulf f0,f1,f2 | PR#6 | PR#3 | c4 | c5 | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
t | 4 | addi r1,4,r1 | PR#7 | PR#4 | c5 |  | 
 | 5 | ldf X(r1),f1 | PR#8 | PR#5 |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#5+
f2 | PR#6
r1 | PR#7
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | yes | addi | PR#7 | PR#4+ | 
2 | LD | no |  |  |  | 
3 | ST | yes | stf |  | PR#6 | PR#4+
4 | FP1 | no |  |  |  | 
5 | FP2 | no |  |  |  | 
CDB
T
undo ldf (ROB#5)
1. free RS
2. free T (PR#8), return to FreeList
3. restore MT[f1] to Told (PR#5)
4. free ROB#5
Free List
PR#2,PR#8 PR#9
insns may execute during rollback
(not shown)

## Slide 57: R10K: Cycle 7 (with precise state)
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
 | 1 | ldf X(r1),f1 | PR#5 | PR#2 | c2 | c3 | c4
h | 2 | mulf f0,f1,f2 | PR#6 | PR#3 | c4 | c5 | 
t | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 | PR#7 | PR#4 | c5 |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#5+
f2 | PR#6
r1 | PR#4+
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | no |  |  |  | 
2 | LD | no |  |  |  | 
3 | ST | yes | stf |  | PR#6 | PR#4+
4 | FP1 | no |  |  |  | 
5 | FP2 | no |  |  |  | 
CDB
T
undo addi (ROB#4)
1. free RS
2. free T (PR#7), return to FreeList
3. restore MT[r1] to Told (PR#4)
4. free ROB#4
Free List
PR#2,PR#8,PR#7, PR#9

## Slide 58: R10K: Cycle 8 (with precise state)
ROB |  |  |  |  |  |  | 
ht | # | Insn | T | Told | S | X | C
 | 1 | ldf X(r1),f1 | PR#5 | PR#2 | c2 | c3 | c4
ht | 2 | mulf f0,f1,f2 | PR#6 | PR#3 | c4 | c5 | 
 | 3 | stf f2,Z(r1) |  |  |  |  | 
 | 4 | addi r1,4,r1 |  |  |  |  | 
 | 5 | ldf X(r1),f1 |  |  |  |  | 
 | 6 | mulf f0,f1,f2 |  |  |  |  | 
 | 7 | stf f2,Z(r1) |  |  |  |  | 
Map Table | 
Reg | T+
f0 | PR#1+
f1 | PR#5+
f2 | PR#6
r1 | PR#4+
Reservation Stations |  |  |  |  |  | 
# | FU | busy | op | T | T1 | T2
1 | ALU | no |  |  |  | 
2 | LD | no |  |  |  | 
3 | ST | no |  |  |  | 
4 | FP1 | no |  |  |  | 
5 | FP2 | no |  |  |  | 
CDB
T
undo stf (ROB#3)
1. free RS
2. free ROB#3
3. no registers to restore/free
4. how is L1-D write undone?
Free List
PR#2,PR#8,PR#7, PR#9

## Slide 59: P6 vs. R10K (Renaming)
R10K-style became popular in late 90’s, early 00’s
  E.g., MIPS R10K (duh), DEC Alpha 21264, Intel Pentium4
P6-style is making a comeback
  Why? Frequency (power) is on the retreat, simplicity is important
Feature | P6 | R10K
Value storage | ARF,ROB,RS | PRF
Register read | @D: ARF/ROB  RS | @S: PRF  FU
Register write | @R: ROB  ARF | @C: FU  PRF
Speculative value free | @R: automatic (ROB) | @R: overwriting insn
Data paths | ARF/ROB  RS RS  FU FU  ROB ROB  ARF | PRF  FU FU  PRF
Precise state | Simple: clear everything | Complex: serial/checkpoint

## Slide 60: Speculation Recovery
Squashing instructions in front-end pipeline
IF
ID
DS
EX
WXYZ
QRST
KLMN
mispred!
nop
nop
nop
nop
nop
nop
nop
nop
EFGH
nop’s are filtered out – no need
to take up RS and ROB entries
???
What about insts
that are already in
the RS, ROB, …?
nop
nop
nop
nop

## Slide 61: Stall and Drain (1/2)
Squash in-order front-end (as before)
Stall dispatch (no new instructions  ROB, RS)
Let OoO engine execute as usual
Let commit operate as usual except:
  Check for the mispredicted branch
    Cannot commit any instructions after it
      Any insns. in pipeline are on the wrong path
    Flush the OoO engine
    Allow dispatch to continue
Notes: This is slow, but to the best of my knowledge this is how it is still done in the Intel-family of processors (it definitely was the case for the original P-Pro according to Bob Colwell’s chapter in Shen and Lipasti’s book).

## Slide 62: Stall and Drain (2/2)
Delays recovery until BR retires
LOAD
ADD
BR
junk
junk
junk
junk
junk
Ideal:
X
X
X
X
X
LOAD
ADD
BR
XOR
LOAD
SUB
ST
BR
Stall & Drain:
LOAD
ADD
BR
junk
junk
junk
junk
junk



- - -
- - -
- - -
junk
junk
junk
junk
junk
X
X
X
X
X
- - -
- - -
- - -
XOR
LOAD
SUB
ST
BR
  Simple to build, but low performance

## Slide 63: Branch Tags/Colors (1/2)
Each insn. assigned the “current” branch tag
Each predicted branch allocates a new branch tag
  Newly allocated tag becomes current
Tags
1
1
1
1
1
2
2
2
2
2
2
2
4
4
4
7
7
7
7
7
5
3
3
3
3
branch
(Tags might not necessarily be in any particular order)
ROB
Notes: The following slides just discuss possible ways in which one could try to attempt to implement faster recovery mechanisms. I’m not aware of any processors that have actually used these.
Tags not being in order could just be due to how the tags are recycled and reassigned.

## Slide 64: Branch Tags/Colors (2/2)
Tags
1
1
1
1
1
2
2
2
2
2
2
2
4
4
4
7
7
7
7
7
5
3
3
3
3
1
Tag List
2
4
7
5
3
ROB
mispred!
7
5
3










Notes: You only broadcast any tags after the mispredicted branch.

## Slide 65: Branch Tags for RS, overkill for ROB
ROB keeps insns. in program order
Squash all insns. after mispredicted branch
Tagging/coloring useful for RS
  Insns. in RS are in arbitrary order
  May be organized into multiple sets of RSs
ROB
Integer RS
FP RS
Notes: Even the “simple” squashing isn’t necessarily that trivial because the buffers are organized as circular queues, and so the circuitry has to properly handle wrap-around.

## Slide 66: Hardware Complexity
my tag
=
=
=
invalidate tag 0
invalidate tag 1
invalidate tag 2
squash
Height increases with
number of branch tags
Width increases with
num branch tags
  Area overhead is quadratic in tag count

## Slide 67: Squash Simplifications (1/2)
For n-entry ROB, could have n different branches
In practice, only a fraction of insns. are branches
  Limit to k < n tags instead
  If k+1st branch is fetched, stall dispatch (structural hazard)
Notes: Worst case: consider if the oldest branch mispredicts and so all subsequent tags have to be broadcasted… now what if all subsequent instructions are branches (one tag each)! That’s a huge amount of broadcasts. Limits on the number of in-flight branches may be needed due to constraints on other resources (e.g., state for recovering speculative branch history register(s) after mispredictions).

## Slide 68: Squash Simplifications (2/2)
For k tags, need to broadcast all younger tags
  Results in O(k2) overhead
Limit to few (e.g., one) broadcast per cycle
7





5

3




Resume
Dispatch
  Can fetch and decode while squashing in back-end
Notes: In this example, recovery takes three cycles instead of one. Note that it’s not necessary to recover in a single cycle… to avoid any performance penalties, you only need to have recovered by the time the newly fetched correct-path instructions make it to the dispatch point in the processor (i.e., if the processor front-end takes 5 cycles from fetch to dispatch, then recovering in 2 cycles doesn’t really buy you anything more than if you took 4 cycles to recover).

## Slide 69: Register Speculation Recovery
br
ARF
RAT
ARF state corresponds to state prior
to oldest non-committed instruction
As instructions are processed, the RAT corresponds to the register mapping after
the most recently renamed instruction
On a branch misprediction, wrong-path
instructions are flushed from the machine
?!?
  RAT left in invalid state

## Slide 70: Solution 1: Stall and Drain
br
ARF
RAT
?!?
Correct path instructions from fetch;
can’t rename because RAT is wrong
foo
X
ARF now corresponds to the state
right before the next instruction to
be renamed (foo)
Allow all instructions to execute and
commit; ARF corresponds to last
comitted instruction
Reset RAT so that all mappings
refer to the ARF
Resume renaming the new correct-
path instructions from fetch
  Simple to build, but low performance
Notes: My understanding is that this is how it is done in the Pentium-Pro family of processors.

## Slide 71: Solution 2: Checkpointing (1/2)
br
br
br
br
ARF
RAT
At each branch, make a copy of the RAT
(register mapping at the time of the branch)
RAT
RAT
RAT
RAT
On a misprediction:
Checkpoint
Free Pool
1. flush wrong-path instructions
2. deallocate RAT checkpoints
3. recover RAT from checkpoint
foo
4. resume renaming
  Squash tags/colors can be same as checkpoints
Notes: Obviously limited by the number of branches… if branches are limited for other reasons (e.g., branch history register checkpoints), then it makes sense to set this limit to be the same.

## Slide 72: Solution 2: Checkpointing (2/2)
No need to stall front-end
  Need to “flash copy” RAT
    Both for making checkpoints and recovering
  Need to recover wrong-path checkpoints
More hardware
  Need one checkpoint per branch
  What if the code has all branches?
    Stall front-end when out of branch colors/checkpoints

## Slide 73: Solution 3: Undo List
Each ROB entry tracks two physical registers
  Its destination register
  The previous physical register mapping
    Required for R10K-style OoO anyway
Walk ROB backwards, applying the old mappings
  Low overhead: don’t need full copies of the RAT
  Slower: need to walk the ROB
  Flexibility: can recover to any instruction
Can combine with checkpointing
  Checkpoint low-confidence branches; walk ROB for others
Notes: My understanding is that the P4 processors did something similar to this?